## Slide 1
EKF Robot Localization Architecture
Planar Ackermann Vehicle - IMU + Wheel Odometry Fusion
Sensor Inputs
Ackermann Steering Controller
Topic: /odom
nav_msgs/Odometry
IMU Sensor
(Gazebo IMU Plugin)
Topic: /imu
sensor_msgs/Imu
robot_localization
ekf_node
Frequency: 50 Hz
2D Mode: Enabled
Fused State Variables:
Odom → x, y, yaw
IMU → yaw, yaw_rate
Outputs
Filtered Odometry
/odometry/filtered
TF Transform
odom → base_link
x, y, yaw
yaw, ω_yaw
Coordinate Frames & Configuration
map
(world frame)
odom
(EKF frame)
base_link
(robot frame)
Launch: ekf_imu_odom.launch.py
Config: config/ekf_imu_odom.yaml
use_sim_time: true | sensor_timeout: 0.5s
Legend:
Sensor
EKF
Output