## Slide 1
EKF: IMU + Odometry Fusion
Extended Kalman Filter for Robot Localization

## Slide 2
What is Extended Kalman Filter (EKF)?
• A recursive state estimation algorithm
• Fuses multiple noisy sensor measurements
• Handles non-linear system dynamics
• Provides optimal estimate of robot pose
• Runs at high frequency (50 Hz in our config)
• Part of robot_localization ROS 2 package

## Slide 3
Why Fuse IMU + Odometry?
• Wheel Odometry alone has drift over time
• IMU alone suffers from integration errors
• Combined: IMU corrects odometry drift!
• IMU provides fast orientation updates (gyroscope)
• Odometry provides position from wheel encoders
• Result: More accurate and robust localization

## Slide 4
Data Flow: Sensor Fusion
IMU (/imu)
Wheel Odom (/odom)
EKF (robot_localization)
Filtered Output (/odometry/filtered)
yaw, yaw_rate
x, y, yaw

## Slide 5
EKF State Vector (15 states)
x: Position X
y: Position Y
z: Position Z
roll: Roll
pitch: Pitch
yaw: Yaw (heading)
vx: Velocity X
vy: Velocity Y
vz: Velocity Z
ωroll: Roll rate
ωpitch: Pitch rate
ωyaw: Yaw rate
ax: Accel X
ay: Accel Y
az: Accel Z
🟢 Used in your config ⚪ Not used (2D planar mode)

## Slide 6
IMU Input Configuration (/imu)
# IMU provides orientation and angular velocity
imu0: /imu
# What we fuse from IMU:
imu0_config: [
false, false, false, # x, y, z - NOT from IMU
false, false, true, # roll, pitch, YAW ✓
false, false, false, # vx, vy, vz - NOT from IMU
false, false, true, # ωroll, ωpitch, ωYAW ✓
false, false, false # ax, ay, az - NOT used
]
# IMU gives us: yaw angle + yaw rate
# Fast updates, good for rotation tracking

## Slide 7
Odometry Input Configuration (/odom)
# Wheel odometry from Ackermann controller
odom0: /odom
# What we fuse from odometry:
odom0_config: [
true, true, false, # X ✓, Y ✓, z
false, false, true, # roll, pitch, YAW ✓
false, false, false, # vx, vy, vz
false, false, false, # ωroll, ωpitch, ωyaw
false, false, false # ax, ay, az
]
# Odometry gives us: x, y position + yaw
# Accurate short-term, drifts over distance

## Slide 8
2D Mode: Planar Robot Simplification
• two_d_mode: true
• Robot moves on a flat surface (ground plane)
• Ignores roll and pitch from IMU
• Only tracks: x, y, yaw, vx, vy, vyaw
• Reduces computational complexity
• Perfect for wheeled robots like RC cars

## Slide 9
TF Frame Configuration
• map_frame: map → Global reference (from SLAM)
• odom_frame: odom → Odometry reference frame
• base_link_frame: base_link → Robot body frame
• world_frame: odom → EKF operates in odom frame
•
• EKF publishes: odom → base_link transform
• SLAM publishes: map → odom transform

## Slide 10
EKF Algorithm: Predict-Update Cycle
• PREDICT: Use motion model to estimate next state
• x̂ₖ = f(x̂ₖ₋₁, uₖ) + process noise
•
• UPDATE: Correct prediction using sensor measurements
• Kₖ = Kalman Gain (how much to trust sensors)
• x̂ₖ = x̂ₖ + Kₖ(zₖ - h(x̂ₖ)) ← Innovation
•
• Runs 50 times per second (50 Hz)

## Slide 11
EKF Output
• Topic: /odometry/filtered
• Message type: nav_msgs/Odometry
•
• Contains:
• • Filtered pose (x, y, z, orientation)
• • Filtered twist (linear & angular velocity)
• • Covariance matrices (uncertainty)
•
• TF: Publishes odom → base_link transform

## Slide 12
Summary: Your EKF Setup
• Fuses: Wheel odometry (/odom) + IMU (/imu)
• Mode: 2D planar (two_d_mode: true)
• Rate: 50 Hz
• From IMU: yaw angle + yaw rate
• From Odom: x, y position + yaw
• Output: /odometry/filtered + TF transform
• Result: Smooth, accurate robot localization!